## Slide 1: The IoT of Automation
A Totally New Way to Look at Control and Automation in the Process Industries
Presented by: Donald C. Clark
VP Industries and Schneider Master Expert Edison Fellow
Process Automation Business
LCCC Process Control Workshop, September 28-30, 2016
Lund University, Lund, Sweden

## Slide 2: “A Control System Without Field Devices is Nothing But a Brain in a Jar…”
This is how we now tend to think of modern industrial control systems…
We’ve forgotten about the field…
We’ve even forgotten about control…
Measurement is no longer mentioned in polite circles…
“They’re just a computer…”
“…just like any other computer…”
When it comes to process control and automation, how should we approach “IoT”?
“…what’s a valve?”

## Slide 3: Introduction
Process control: to keep a process safe and operating to design to produce economic value for the asset owners…
…has been with us since the earliest days of the industrial revolution…and…
…will always persist…and will never go away.
How we solve/address those challenges – the platform on which the control is executed – ie the “automation”…
…has changed over time…and will radically change in the future.
The “intelligence” to achieve this objective is being pushed further and further “down” the architecture, and the traditional process control “Levels” are being compressed over time closer to the valve and the sensor…and to the process itself.
There will ALWAYS be the conversion process itself…and its process equipment: pipes, vessels, pumps, reactors, concrete, steel, catalysts, etc., but how to control that process has – and will continue – to dramatically shift over time.

## Slide 4
Control Room
Process Connected
Compact I/O
Redundant
Controllers
Control Network
Modicon
Integrated
Control
Maintenance
Station
Engineering
Station
Applications Processor
Operator Station
Modicon
Remote and local I/O
Modicon I/O bus
Foxboro
Remote and local
Control
I/O network
State-of-the-Art Industrial Control System
Modbus
1. Over time…
Number of controllers needed per system
Amount of control per controller
– for Four Decades
No longer considered “distributed”
Risk of exposure for failure
2. Were severely limited in their scope by the technologies available:
  Manual/direct human manipulation/intervention in the process
  Mechanical control (e.g. spinning ball governors, siphon level control)
  Pneumatic (huge benefit: intrinsically safe)
  Electronic
  Digital computing and microprocessors
Forced control to be applied on the process, as an add-on or an appendage to the process
New technologies will bring the ability to shift that century-old paradigm so that control will be performed in the process, in-situ, in the actual process devices and equipment needed for the process, not “stuck-on”.
It will become embedded and autonomous in a way to mimic what in fact occurs in the control of biological processes such as the human body: the process controls itself, it is NOT “stuck-on”.
time
The predicament we’re in:

## Slide 5: The Common Core Functionality (CCF)
I/O
Display
CPU
Comms
Has been utilized for decades to architect control systems
The “controller” of any brand of DCS today
…and for the past 40 years
The economies of scale and time/technology curves has put us in the predicament we’re in
“…it’s just a computer…”

## Slide 6: But: Available Technology Can Now…
I/O
Display
CPU
Comms
…put this on a chip…
…for about $3…
…to do about 8 things
Empowers a totally new way to look at control
Allows us to return to our roots…
Performs “a few” Control Instrumented Functions (CIF)
…very rugged…
…very low power
…harvest power needed
…the size of a postage stamp
Schneider is already developing this!!

## Slide 7: Imagine Instead…
Core Velocity
Spinal Cord – High-Speed Control & I/O Network
Batch Box
Analog Box
History Box
App Box
Enterprise Service Bus (ESB)
IM
Triconex
I/O System
IM
IA series
I/O System
IM
PAC
I/O System
IM
3rd Party PLC
&
Control Safety
I/O System
IM-S
Safety I/O
IM
FF HART
IEC61850 Devicenet
Profibus
IM
Universal I/O
Loop I/O
Operator Decision Support Centre
Eyes
Web
Operator Station
Unified Configuration Environment
Scalable Availability
App Engines
Foreign Operator Stations (Local or Remote)
Unified Configuration Environment
To other Units
To other Units
Existing Platform Integration
Unified Configuration Environment
IM
SCADA
I/O System
IM
High Density
I/O
IM
Other I/O ?
IM
MTU
R-IM
Various I/O
R-IM
Various I/O
Minimum Velocity
Up to 5K points per process cell
I/O Personality
Display Optional
CPU
Comms Personality
Spinal Cord – High-Speed Control & I/O Network
Spinal Cord – High-Speed Control & I/O Network
1. Reduce CCF to the granularity of one, $3, and size of postage stamp: CPS
Equipment fog– High-Speed communications Network – meshed together
2. Low-level "fog" of communications "clinging" to the equipment via meshing
Intrinsically secure/immune to hacking by distance
Core Velocity
Up to 5K points per process cell
I/O Personality
Display Optional
CPU
Comms Personality
3. Use power harvested from surroundings
“Cyber Physical System” (CPS)
4. Control now occurs at the asset

## Slide 8: Now in a Plant Today…
Traditional process sensing and outputs are “stuck on” to the process…
…and traditionally unmeasured devices…
…that are an integral part of the process…
…that are mini-processes in themselves…
…are usually treated as stupid (because they are), or just ignored…
And the controllers are even further removed from the process in the MCC
Today, the hierarchical equipment relationships that form the process must be implemented – and maintained – by people. That model is constructed for the system, not by the system
= traditional process sensors & outputs/valves
= process equipment: e.g. pumps, reactors, etc.

## Slide 9: How Control at the Asset Will Change This…
I/O Personality
Display Optional
CPU
Comms Personality
…communicating via the secure highly localized communications fog
Put measurement/control/comms CCF inside conventional sensors & valves…
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
…handling routine process control – most usually with nearest neighbors
…as well as asset performance management - avatars
…aware of environment – self configuring (ie modeling). No need to keep models
As defined by the device vendor
For Traditional Process Sensing and Outputs…
Autonomous

## Slide 10: The Same Can Be Done For Traditionally Unmeasured Devices…and Equipment
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
… communicating via the intrinsically secure highly localized fog of communications
Put measurement/control/comms CCF inside the asset…
…handling routine process control – most usually with nearest neighbors
…as well as asset performance management - avatars
…aware of environment – self configuring (ie modeling). No need to keep models
As defined by the equipment vendor
…as complex as a FCC power recovery turbine..
…or as humble as a length of pipe (or act as repeater)
…empowering equipment at the very edge of the process
…with the vendor’s IP – they know their equipment the best
Autonomous

## Slide 11: So Now Our Plant Looks Like…
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
Wireless Spinal Cord – High-Speed Control & I/O Network
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
I/O Personality
Display Optional
CPU
Comms Personality
…all meshed together communicating via the highly localized fog of communications that “clings” to the process equipment only
Wireless Spinal Cord – High-Speed Control & I/O Network
Batch Brain
Analog Brain
Pain Centre
Voice Box
Enterprise Service Bus (ESB)
Operator Decision Support Centre
Eyes
Web
Operator Station
Unified Configuration Environment
App Engines
Non-Velocity Operator Stations (Local or Remote)
Unified Configuration Environment
To other Units
To other Units
Unified Configuration Environment
Control Room
Harness “WinTel”/Internet domain
Process Connected
With a control granularity approaching one
Totally and truly “distributed control”
Self identifying and autonomous to reduce configuration and modeling costs
Built-in security
Fail-safe robustness and redundancy only where needed
Provides unprecedented scalability
“Control” is sold with the equipment itself, not “stuck-on”
Provides inherent asset performance intelligence
The “Internet of Things” as it applies to automation

## Slide 12: Immediate Benefits
Allows for lower cost, and much more resilient and robust control as it is so close to the process, not removed/separated from it.
Redundancy granularity of one within control clusters
Self-identifying and autonomous - minimizing/eliminating configuration and modeling at control level. Any change is automatically accommodated.
Low power – can use power harvesting for needed power
Minimal/no wiring, intrinsically cyber-secure networks that follows the process
Equipment vendors impart their asset performance knowledge within device:
  First-level process control
  Asset control of the process devices and equipment themselves
  Asset performance of the process will become the norm and routine

## Slide 13: Commercial Strategy…
    Schneider’s focus remains at the systems level
    Begin at the measurement and valve levels:
        Add to our own – and other’s – sensor, analytical, and valve portfolios:
        We add intelligence to otherwise stupid assets to the device OEMs, adding:
          Diagnostics
          Communications
          Measurement
          Control
        Provides IP in the form of location (in device), number, type, & asset performance IP in the device
      Expand to equipment providers: they provide their IP as avatars on the CPS’s
      Current architectures can accommodate this technology allowing for systems to be a combination of current and this technology
      Move from process efficiency control to business performance control
      Traditional “advanced” functionality operating over a wide-range of assets will still be provided at the system level communicating over the fog
System software is key to this:
Devices are not stand-alone; are part of a system
Reliant on open, interoperable industry Standards (ISA95, OG):
  Functionality/naming definitions
  Communications
Create a “system of systems”
Each CPS has a bit of “system”: build the system CPS by CPS
Notes: Bold subheadlines [from Slide Master]
Subheadlines may be applied in Verdana Bold. These should be the same size as the body text to which they apply and should not use highlight colours or any different styling or type attributes.

## Slide 14: Summary
Essentially takes conventional automation systems, chops it up to smallest granularity possible, and distributes around the process in the actual process devices and equipment, all powered by harvested power, communicating in a fog of combined meshes, operating within a unifying systems framework
Control is no longer “stuck on” – it is in situ, autonomous, part of the process
Control shifts to the device itself with added device IP by vendor
The plant models itself: control perfectly represents the actual plant
Schneider focuses on what it does best: providing the system characteristics
Maximum security, reliability and resiliency at lowest possible cost
This is the Internet of Things as applied to industrial process control:
It is functionality, not connectivity

## Slide 15: Tack